## Slide 1: Memory Hierarchy and Caches
Don Porter
Lecture 15

## Slide 2: Topics
Memory Flavors
Principle of Locality
Memory Hierarchy: Caches
Associativity
Reading: Ch. 5.1-5.3

## Slide 3: What Do We Want in a Memory?
PC
INST
MADDR
MDATA
miniMIPS
MEMORY
 | Capacity | Latency | Cost
Register | 1000s of bits | 10 ps | $$$$
SRAM | 1-8 MBytes | 0.5-1 ns | $2K/GB
DRAM | 1-8 GBytes | 50 ns | $20/GB
Hard disk* | 100s GBytes | 10 ms | 20¢/GB
Want? | Huge | Low (fast) | Cheap!
*non-volatile: Typically magnetic disk drive, but also SSD/flash now
ADDR
DOUT
ADDR
DATA
R/W
Wr

## Slide 4: Best of Both Worlds
What we REALLY want: A BIG, FAST memory!
  Keep everything within instant access
We’d like to have a memory system that
  Stores 2-16 GB of data like DRAM would
    typical SRAM sizes are in MB, not GB
  Performs fast like SRAM would
    typical DRAMs are order of magnitude slower than SRAM
  SURPRISE: We can (nearly) get our wish!
    Key Idea: Use a hierarchy of memory technologies:
CPU
SRAM
MAIN
MEM
(DRAM)
DISK

## Slide 5: Principle of Locality
Key Idea: Exploit “Principle of Locality”
  Keep data used often in a small fast SRAM
    called “CACHE”, often on the same chip as the CPU
  Keep all data in a bigger but slower DRAM
    called “main memory”, usually separate chip
  Access Main Memory only rarely, for remaining data
  The reason this strategy works: LOCALITY
    if you access something now, you will likely access it again (or its neighbors) soon
Locality of Reference:
Reference to location X at time t implies that reference to location X+X at time t+t is likely for small X and t.
Put simply: If a location is accessed in memory, the same location or its neighbors will likely be accessed soon.

## Slide 6: Typical Memory Reference Patterns
Memory Trace
  A temporal sequence of memory references (addresses) from a real program.
Temporal Locality
  If an item is referenced, it will tend to be referenced again soon
Spatial Locality
  If an item is referenced, nearby items will tend to be referenced soon.
time
address
data
stack
program
Notes: Program trace: Typically runs of sequential instructions, with intervening branches. Repeated runs are because of loops.
Data trace: Runs of sequential accesses are typically because of stepping through arrays.
Stack: Pushes and pops to/from stack mean no sudden breaks in access pattern.

## Slide 7: Cache
cache (kash) n.
  A hiding place used especially for storing provisions.
  A place for concealment and safekeeping, as of valuables.
  The store of goods or valuables concealed in a hiding place.
  Computer Science. A fast storage buffer in the central processing unit of a computer. In this sense, also called cache memory.
v. tr. cached, cach·ing, cach·es.
  To hide or store in a cache.

## Slide 8: Cache Analogy
You are writing a term paper for your history class at a table in the library
  As you work you realize you need a book
  You stop writing, fetch the reference, continue writing
  You don’t immediately return the book, maybe you’ll need it again
  Soon you have a few books at your table, and you can work smoothly without needing to fetch more books from the shelves
  The table is a CACHE for the rest of the library
Now you switch to doing your biology homework
  You need to fetch your biology textbook from the shelf
  If your table is full, you need to return one of the history books back to the shelf to make room for the biology book

## Slide 9: Exploiting the Memory Hierarchy
Memory Hierarchy is hidden from programmer!
  Programming model: SINGLE kind of memory, single address space.
  Transparent to programmer: Machine AUTOMATICALLY assigns locations, depending on runtime usage patterns.
    programmer doesn’t (cannot) know where the data is actually stored!
CPU
Small
SRAM
Dynamic
RAM
HARD
DISK
“MAIN MEMORY”
“CACHE”
Notes: Modern OSs follow Approach 2, so programmer is relieved of burden of managing data movement between different levels of hierarchy. This allows the program to be written independently of the actual size of cache and main memory, so increases portability.
The hard disk shown in this picture is not intended for storing files and folders. Instead a portion of the hard disk is set aside for the CPU and OS to store “spillover” data that is needed by running programs but cannot fit in the main memory. This portion of the hard disk provides a storage capability called “Virtual Memory”. On Windows, it may be the file pagefile.sys, on Unix it may be the /swap partition. This is distinct from the files/folders of your file system.

## Slide 10: Exploiting the Memory Hierarchy
CPU speed is dominated by memory performance
  More significant than: ISA, circuit optimization, pipelining, etc.
  TRICK #1: Make slow MAIN MEMORY appear faster
    Technique: CACHING
  TRICK #2: Make small MAIN MEMORY appear bigger
    Technique: VIRTUAL MEMORY
CPU
Small
SRAM
Dynamic
RAM
HARD
DISK
“MAIN MEMORY”
“VIRTUAL MEMORY”
“SWAP SPACE”
“CACHE”
Notes: The hard disk shown in this picture is not intended for storing files and folders. Instead a portion of the hard disk is set aside for the CPU and OS to store “spillover” data that is needed by running programs but cannot fit in the main memory. This portion of the hard disk provides a storage capability called “Virtual Memory”. On Windows, it may be the file pagefile.sys, on Unix it may be the /swap partition. This is distinct from the files/folders of your file system. In a way, the main memory is a “cache” for the virtual memory.

## Slide 11: The Cache Idea
Program-Transparent Memory Hierarchy:
  Cache contains TEMPORARY COPIES of selected main memory locations…
    e.g. Mem[100] = 37
Two Goals:
  Improve the average memory access time
    HIT RATIO (⍺): Fraction of refs found in cache
    MISS RATIO (1- ⍺): Remaining references
    avg total access time depends on these parameters
  Transparency (compatibility, programming ease)
1.0
(1.0-)
CPU
Cache
DYNAMIC
RAM
Main Memory
100 37
Challenge:
To make the hit ratio as high as possible.
Notes: t_c is the time needed to look an address up in the cache (whether hit or miss).
t_m is the time needed to read a value from main memory.

## Slide 12: How High of a Hit Ratio?
Suppose we can easily build a cache with a 0.8 ns access time, but the fastest RAM we can buy for main memory has access time of 10 ns. How high of a hit rate do we need to sustain an average total access time of 1 ns?
Wow, a cache really needs to be good!

## Slide 13: Cache
Sits between CPU and main memory
Basically a fast table that stores a TAG and DATA
  TAG is the memory address
  DATA is a copy of memory contents at the address given by TAG
1000 | 17
1040 | 1
1032 | 97
1008 | 11
1000 | 17
1004 | 23
1008 | 11
1012 | 5
1016 | 29
1020 | 38
1024 | 44
1028 | 99
1032 | 97
1036 | 25
1040 | 1
1044 | 4
Main Memory
Tag
Data
Cache

## Slide 14: Cache Access
On load (lw) we look in the TAG entries for the address we’re loading
  Found  a HIT, return the DATA
  Not Found  a MISS, go to memory for the data and put it and the address (TAG) in the cache
1000 | 17
1040 | 1
1032 | 97
1008 | 11
1000 | 17
1004 | 23
1008 | 11
1012 | 5
1016 | 29
1020 | 38
1024 | 44
1028 | 99
1032 | 97
1036 | 25
1040 | 1
1044 | 4
Main Memory
Tag
Data
Cache

## Slide 15: Cache Lines
Usually get more data than requested
  a LINE is the unit of memory stored in the cache
  usually much bigger than 1 word, 32 bytes per line is common
  bigger LINE means fewer misses because of spatial locality
  but bigger LINE means longer time on miss
1000 | 17 | 23
1040 | 1 | 4
1032 | 97 | 25
1008 | 11 | 5
Tag
Data
1000 | 17
1004 | 23
1008 | 11
1012 | 5
1016 | 29
1020 | 38
1024 | 44
1028 | 99
1032 | 97
1036 | 25
1040 | 1
1044 | 4
Main Memory
Cache

## Slide 16: Finding the TAG in the Cache
Fully Associative:
  Requested data could be anywhere in the cache
  Fully Associative cache uses hardware to compare the address to the tags in parallel but it is expensive
    1 MB is thus unlikely, typically smaller
Direct Mapped Cache:
  Directly computes the cache entry from the address
    multiple addresses will map to the same cache line
    use TAG to determine if right
  Choose some bits from the address to determine cache entry
    low 5 bits determine which byte within the line of 32 bytes
    we need 15 bits to determine which of the 32k different lines has the data
    which of the 32 – 5 = 27 remaining bits should we use?

## Slide 17: Direct-Mapping Example
Suppose: 2 words/line, 4 lines, bytes are being read
  With 8 byte lines, bottom 3 bits determine byte within line
  With 4 cache lines, next 2 bits determine which line to use
    1024d = 10000000000b  line = 00b = 0d
    1000d = 01111101000b  line = 01b = 1d
    1040d = 10000010000b  line = 10b = 2d
1024 | 44 | 99
1000 | 17 | 23
1040 | 1 | 4
1016 | 29 | 38
Tag
Data
1000 | 17
1004 | 23
1008 | 11
1012 | 5
1016 | 29
1020 | 38
1024 | 44
1028 | 99
1032 | 97
1036 | 25
1040 | 1
1044 | 4
Main memory
Cache

## Slide 18: Direct Mapping Miss
What happens when we now ask for address 1008?
    1008d = 01111110000b  line = 10b = 2d
  …but earlier we put 1040d there
    1040d = 10000010000b  line = 10b = 2d
  …so evict 1040d, put 1008d in that entry
1024 | 44 | 99
1000 | 17 | 23
1040 | 1 | 4
1016 | 29 | 38
Tag
Data
1000 | 17
1004 | 23
1008 | 11
1012 | 5
1016 | 29
1020 | 38
1024 | 44
1028 | 99
1032 | 97
1036 | 25
1040 | 1
1044 | 4
Memory
1008 | 11 | 5
Cache

## Slide 19: Miss Penalty and Rate
How much time do you lose on a Miss?
  MISS PENALTY is the time it takes to read the main memory if data was not found in the cache
    50 to 100 clock cycles is common
  MISS RATE is the fraction of accesses which MISS
  HIT RATE is the fraction of accesses which HIT
  MISS RATE + HIT RATE = 1
Example
  Suppose a particular cache has a MISS PENALTY of 100 cycles and a HIT RATE of 95%. The CPI for load on HIT is 5 but on a MISS it is 105. What is the average CPI for load?
    Average CPI = 5 * 0.95 + 105 * 0.05 = 10
  What if MISS PENALTY = 120 cycles?
    Average CPI = 5 * 0.95 + (120+5) * 0.05 = 11

## Slide 20: Continuum of Associativity
N
address
N-way set associative
Compares addr with N tags simultaneously. Data can be stored in any of the N cache lines belonging to a “set” like N direct-mapped caches.
address
Fully associative
Compares addr with ALL tags simultaneously location A can be stored in any cache line.
address
Direct-mapped
Compare addr with only ONE tag. Location A can be stored in exactly one cache line.
Finds one entry out of entire cache to evict
What happens on a MISS?
Finds one entry out of N in a particular row to evict
There is only one place it can go

## Slide 21: Three Replacement Strategies
When an entry has to be evicted, how to pick the victim?
  LRU (Least-recently used)
    replaces the item that has gone UNACCESSED the LONGEST
    favors the most recently accessed data
  FIFO/LRR (first-in, first-out/least-recently replaced)
    replaces the OLDEST item in cache
    favors recently loaded items over older STALE items
  Random
    replace some item at RANDOM
    no favoritism – uniform distribution
    no “pathological” reference streams causing worst-case results
    use pseudo-random generator to get reproducible behavior

## Slide 22: Handling WRITES
Observation: Most (80+%) of memory accesses are reads, but writes are essential. How should we handle writes?
  Two different policies:
    WRITE-THROUGH: CPU writes are cached, but also written to main memory (stalling the CPU until write is completed). Memory always holds the latest values.
    WRITE-BACK: CPU writes are cached, but not immediately written to main memory. Main memory contents can become “stale”. Only when a value has to be evicted from the cache, and only if it had been modified (i.e., is “dirty”), only then it is written to main memory.
  Pros and Cons?
    WRITE-BACK typically has higher performance
    WRITE-THROUGH typically causes fewer consistency problems

## Slide 23: Memory Hierarchy Summary
Give the illusion of fast, big memory
  small fast cache makes the entire memory appear fast
  large main memory provides ample storage
  even larger hard drive provides huge virtual memory (TB)
Various design decisions affect caching
  total cache size, line size, replacement strategy, write policy
Performance
  Put your money on bigger caches, then bigger main memory.
  Don’t put your money on CPU clock speed (GHz) because memory is usually the culprit!